## Slide 1
RELIABILITY DEMONSTRATION OF PUSH BUTTONS
Presented by
LT CDR ARAVIND MANIKANDAN (25RE61D01)
KADIMI TARUN (25RE61R05)
SUTAMA SARKAR (25RE61R07)
IIT KHARAGPUR
SCSQR
SPRING (2025-26)
9 April 2026

## Slide 2: SCOPE
Test procedure
Binomial sequential test plan
Test observations
Summary of observations
9 April 2026
Indian Institute of Technology, Kharagpur
2
Objective
Introduction
Test operating conditions
Test Setup
Accelerated life testing

## Slide 3
9 April 2026
Indian Institute of Technology, Kharagpur
3
Objective
Introduction
Test operating conditions
Test Setup
Accelerated life testing

## Slide 4: Why Push Button Reliability is Important?
Push buttons are widely used in safety-critical and industrial applications:
Industrial control panels
Railway signalling systems
Medical devices
Automotive dashboards Emergency shutdown systems
Failure of push buttons can lead to:
System malfunction
Safety hazards
Production downtime
Increased maintenance cost

## Slide 5: OBJECTIVE
To demonstrate the minimum acceptable reliability of push button switches for a specified operating time with given Producer’s and Consumer’s Risk
9 April 2026
Indian Institute of Technology, Kharagpur
5

## Slide 6: KEY FACTORS IN RELIABILITY DEMONSTRATION
9 April 2026
Indian Institute of Technology, Kharagpur
6
Define
Define Ru
Define RL
Risk
Set Producer’s risk (α)
Scale
Sample size
Total test time
Environment
Choose normal operating conditions or
Accelerated testing
Method
Pick test design
Set Consumer’s risk (β)
INTRODUCTION

## Slide 7: TYPES OF PUSH BUTTONS
9 April 2026
Indian Institute of Technology, Kharagpur
7
Push button
Switch that operates when pressed
Momentary Push button
Works only when pressed
Latching Push button
Stays ON or OFF after pressing
Based on Operation
Based on Contact type
Normally Open (NO)
Circuit closes when pressed
Normally Closed (NC)
Circuit opens when pressed

## Slide 8: PUSH BUTTON SPECIFICATIONS AND OPERATING CONDITIONS
9 April 2026
Indian Institute of Technology, Kharagpur
8
Parameters / specifications | Description
Switch Type | Push Button Momentary, Roundhead
Terminal Style | Screw type
Operating Temp. | 10oC to 80oC
Mounting | Panel, screw type
Current & Voltage Rating | 5A, 220 V AC
TEST OPERATING CONDITIONS | 
Electrical Supply | 220 V AC supply
Temperature | 25 C
Cycles per minute | 30
Relative Humidity | 70 – 80 % (approx.)
SPST PUSH BUTTON -SE952 PUSH TO ON MEDIUM

## Slide 9
9 April 2026
Indian Institute of Technology, Kharagpur
9

## Slide 10: A QUICK RECAP TO RELIABILITY ENGINEERING LAB OUTPUTS

## Slide 11: FAULT TREE DIAGRAM FOR A PUSH BUTTON FAILURE
9 April 2026
Indian Institute of Technology, Kharagpur
11

## Slide 12: TEST SETUP
Circuit Diagram of the test setup
Actual Test Setup
The circuit was connected as shown in the circuit diagram above. The circuit is designed in such a way that the failure of the switches can be accelerated by either increasing the rate of switching speed (on - off cycle) in rated load conditions or by increasing the load.
9 April 2026
Indian Institute of Technology, Kharagpur
12

## Slide 13: RESULTS FROM RT LAB - ALT
Accelerated stress (A) | Shape parameter (β) | Scale parameter (θ)
0.8 | 2.6063 | 16974.67
1 | 2.6017 | 8409.926
1.5 | 3.9023 | 5621.732
Using Inverse Power Law:
Stress (S) | Beta avg | Theta (θ) | Ln eta (ln θ) | Ln S
0.8 | 3.036767 | 16787.26 | 9.728376 | -0.22314
1 | 3.036767 | 8505.405 | 9.048457 | 0
1.5 | 3.036767 | 5336.599 | 8.582344 | 0.405465
Stress (S) |  | Theta (θ) | Ln eta (ln θ) | Ln S
0.8 | 3.036767 | 16787.26 | 9.728376 | -0.22314
1 | 3.036767 | 8505.405 | 9.048457 | 0
1.5 | 3.036767 | 5336.599 | 8.582344 | 0.405465
9 April 2026
Indian Institute of Technology, Kharagpur
13

## Slide 14: RESULTS FROM RT LAB - ALT (Contd.)
Chart: Ln(eta) vs Ln(S)
| -0.22314355131420971 | 0 | 0.40546510810816438
LN THETA | 9.7284 | 9.0485 | 8.5823
From plot:
Ln A = 9.2256
A = 10153.76651
B = 1.7414
9 April 2026
Indian Institute of Technology, Kharagpur
14
Conditions | Stress (S) | Life (theta) | AF | MTTF | t (test)
Nominal | 0.2 | 167422.39 | 1 | 149585.8 | 30000
case 1 | 0.8 | 14975.67 | 11.17962584 | 13380.21 | 2683.452955
case 2 | 1 | 10153.767 | 16.48869807 | 9072.019 | 1819.428064
case 3 | 1.5 | 5011.6629 | 33.40655439 | 4477.738 | 898.0273646
Electrical life = 30000 cycles
Life (L) = θ =
Acceleration Factor (AF) =
MTTF = θ
t(test) = required testing time or cycles
=
Parameters | Value
Electrical life (cycles) | 30000
Nominal stress (A) | 0.2
theta | 167422.3902
Reliability (Ru) | 0.994613614

## Slide 15: RELIABILITY DEMONSTRATION TESTS

## Slide 16: RELIABILITY DEMONSTRATION TESTS
Binomial Test
Sample size fixed before hand
Allowed no of failures decided before hand
Example: Test 50 push buttons Accept product if failures ≤ 2
Decision is made only after all tests are completed
For high reliability components like push buttons, failures are rare, so testing many samples becomes inefficient
Sequential Test
Testing is done step by step
After each trial, a decision to accept/reject/ continue taken
Advantages
Requires few samples
Reduces cost
Efficient Method

## Slide 17: BINOMIAL DEMONSTRATION PLAN (COMPARISON)
Good product should be accepted with probability ≥
(1-RU)xRUn-x ≥1−α
Bad product should be accepted with probability < β
(1-RL)xRLn-x < β
Parameters | Values | No. of Failures (x) | Total Sample Size (n)
Desired Reliability, RU | 0.99 | 0 | n< 22 n≥31
Min Reliability, RL | 0.95 |  | 
Producer’s Risk, α | 0.2 | 1 | n~59
Consumer’s Risk, β | 0.2 |  | 

## Slide 18: ASSUMPTIONS
All switches are from same manufacturer/lot/batch
Test Equipments are serviceable
Failure mechanism same at normal and accelerated stress
Samples are identical and independent
Operating conditions remain constant
Pass/fail criteria clearly defined
No external disturbances (vibrations)

## Slide 19
Test procedure
Sequential test plan
Test observations
Summary of observations
9 April 2026
Indian Institute of Technology, Kharagpur
19

## Slide 20
TEST PROCEDURE
A Sequential Test Plan is selected for this analysis due to its efficiency in evaluating the system's reliability by minimizing the average sample size while maintaining statistical rigor.
The term sequential indicates that this type of test is accomplished by conducting a succession, or a sequence of runs on one or more devices.
One of the following three decisions is made after each test run,
  Accept: The device has demonstrated the reliability requirement.
  Continue Testing: The status of the device’s reliability is undetermined.
  Reject: The device has failed to demonstrate the reliability requirement
9 April 2026
Indian Institute of Technology, Kharagpur
20

## Slide 21
SEQUENTIAL TEST PLAN
To use the sequential testing analysis technique, four quantities need to be specified RU, RL, 𝛼 and 𝛽.
Two additional terms used here are: QL=1− RU and QU =1− RL
Parameters required | Description
RU | Design objective for the reliability level Reliability obtained from ALT
RL | Minimum acceptable reliability level to the customer. Reliability we want to demonstrate
𝛼 | Producer’s risk Risk of having equipment that has a true reliability equal to or greater than the contract’s design objective rejected
𝛽 | Consumer’s risk Risk of having equipment that has a true reliability less than the minimum required gets accepted
The consumer’s risk, , is associated with the minimum acceptable reliability,
The producer’s risk , is associated with the design objective reliability, .
9 April 2026
Indian Institute of Technology, Kharagpur
21

## Slide 22
SEQUENTIAL TEST PLAN (Contd.)
9 April 2026
Indian Institute of Technology, Kharagpur
22
The following step-by-step method may be used to construct a sequential testing plan to demonstrate that a device meets or fails to meet a specified, acceptable minimum reliability, RL.
Define RU and RL
Define 𝛼 and 𝛽
Determine the value of the accept intercept.
4) Determine the value of the reject intercept.
5) Determine the value of the slope of the test plan lines.
6) Determine the equations for the accept line,
7) Determine the equations for the reject line,

## Slide 23
TEST OBSERVATIONS
9 April 2026
Indian Institute of Technology, Kharagpur
23
RU = 0.99 and RL = 0.95 (consumer grade & industrial grade)
QL=1− 0.99 = 0.01 and QU =1− RL =1− 0.95 = 0.05
𝛼 = 0.2 and 𝛽 = 0.2
= 0.83983
= = 0.83983
= = 0.025
Accept line : = 0.83983 + 0.025 N
Reject line : = 0.83983 + 0.025 N
N | reject line | accept line
1 | 0.864817 | -0.814846
2 | 0.889803 | -0.789861
3 | 0.914788 | -0.764876
4 | 0.939774 | -0.73989
5 | 0.964759 | -0.714905
6 | 0.989744 | -0.689919
7 | 1.01473 | -0.664934
8 | 1.039715 | -0.639948
9 | 1.064701 | -0.614963
10 | 1.089686 | -0.589978
. . . | . . . | . . .

## Slide 24
TEST OBSERVATIONS (Contd.)
9 April 2026
Indian Institute of Technology, Kharagpur
24
Chart: Sequential testing
Minimum number of trials for an accept decision (
0 = 0.83983 + 0.025 N
N = 34 samples
= (6, 6, 6, 6, 6, 4)
Testing cycles for reliability demonstration (T)
= Electrical life / AF
= 30,000 / 11.18
= 2683 cycles
≈ 2700 cycles

## Slide 25
TEST OBSERVATIONS (Contd.)
9 April 2026
Indian Institute of Technology, Kharagpur
25
Sample No. | TTF (Cycles) | Sample No. | TTF (Cycles) | Sample No. | TTF (Cycles)
1 | All push buttons operated satisfactorily upto 2700 cycles | 13 | All push buttons operated satisfactorily upto 2700 cycles | 25 | All push buttons operated satisfactorily upto 2700 cycles
2 |  | 14 |  | 26 | 
3 |  | 15 |  | 27 | 
4 |  | 16 |  | 28 | 
5 |  | 17 |  | 29 | 
6 |  | 18 |  | 30 | 
7 |  | 19 |  | 31 | 
8 |  | 20 |  | 32 | 
9 |  | 21 |  | 33 | 
10 |  | 22 |  | 34 | 
11 |  | 23 |  | X | 
12 |  | 24 |  | X | 

## Slide 26: CONCLUSION
9 April 2026
Indian Institute of Technology, Kharagpur
26
From the sequential testing plot, it is observed that the acceptance line intersects the trial axis at 34, indicating that acceptance is achieved with 0 failures up to 34 samples.
The absence of failures during the test till 2700 cycles indicates that the push buttons exhibit high reliability under the given operating conditions.
The product satisfies the required reliability limits (RL = 0.95) within the specified producer’s and consumer’s risk levels.
The sequential testing method efficiently validates reliability using a minimum number of samples, thereby reducing testing time.
Hence, the push buttons are considered reliable and suitable for practical applications within the specified limits.

## Slide 27: FINAL RELIABILITY STATEMENT
9 April 2026
Indian Institute of Technology, Kharagpur
27
The push button switches exhibited a min Reliability of 0.95 for 2700 cycles with Producer’s and Consumer’s Risk at 20% under stress current of 0.8A

## Slide 28
THANK YOU
9 April 2026
Indian Institute of Technology, Kharagpur
28