## Slide 1
RELIABILITY ASSESSMENT OF JQC‑3FC (T73) SPDT RELAY
PRESENTED BY –
LT CDR ARAVIND MANIKANDAN (25RE61D01)
KADIMI TARUN (25RE61R05)
SUTAMA SARKAR (25RE61R07)
RELIABILITY TESTING LABORATORY
AUTUMN SEMESTER 2025-26
1

## Slide 2
1. Introduction
2. Test Methodology
3. Data Modelling (Weibull + Arrhenius)
4. Results and Reliability Estimates
5. Inferences
6. Conclusions
7. Recommendations
Scope
2

## Slide 3
Introduction
Relay Model
Stress
Temperatures
DL JQC‑3FC (T73)
DC05V (5‑pin, blue casing)
Mechanical life : 10 million cycles
403 K, 393 K, 363 K
Load
1A resistive (10 bulbs), 5s ON / 10s OFF duty cycle
Goal
Estimate lifetime
and reliability
at normal use condition
OBJECTIVE: Assess relay lifetime using elevated-temperature ie accelerated testing.
3

## Slide 4
Introduction
Relay Main Circuit Board
Preparation of Test Set Up
Thermal Chamber

## Slide 5
01
02
Data collected at 3 temperatures until failure
Probability Paper Plotting to determine best dstr fit
Test Methodology
03
Common β applied using pooled estimation
04
Arrhenius model used: ln(θ) vs 1/T
05
Activation Energy (Ea) and Acceleration Factors (AF) computed
5

## Slide 6
Circuit Diagram
R=Relay
B=Bulb
L=Indicators
6

## Slide 7
Test Result
Test data at 403K
Test data at 393K
Relay No. | Failure times (cycles)
R2 | 2724
R9 | 3324
R6 | 3765
R5 | 4457
R10 | 5433
R1 | 6088
R3 | 6822
R4 | 7699
R8 | 8250
R7 | 8542
Relay No. | Failure times (cycles)
R2 | 3022
R10 | 3627
R4 | 4956
R7 | 5416
R3 | 6612
R1 | 7210
R5 | 8342
R8 | 9076
R6 | 10549
R9 | 11351
Test data at 363K
Relay No. | Failure times (cycles)
R1 | 5568
R9 | 7123
R4 | 8476
R6 | 9920
R8 | 11042
R3 | 12457
R2 | 13843
R7 | 15321
R5 | 16455
R10 | 17863
All failures are observed in short circuit mode

## Slide 8
Distribution Fitting of the Failure Times using Least Square Estimation (LSE) Method
LSE of Failures Observed at 403K
8
Chart: Weibull
| 7.9098566672694028 | 8.1089241559753393 | 8.233503140233994 | 8.4022311729465553 | 8.6002467465515231 | 8.7140748995415223 | 8.8279079629785908 | 8.9488457292780499 | 9.0179684793287258 | 9.0527504514014119
Weibull y | -2.6638 | -1.7233 | -1.202 | -0.82167 | -0.5086 | -0.23037 | 0.032925 | 0.29903 | 0.59398 | 0.99269
Chart: Exponential
| 2724 | 3324 | 3765 | 4457 | 5433 | 6088 | 6822 | 7699 | 8250 | 8542
Exponential y | 0.06968 | 0.17848 | 0.30059 | 0.4397 | 0.60134 | 0.79424 | 1.0335 | 1.3486 | 1.8112 | 2.6985
Chart: Log Normal
| 7.9098566672694028 | 8.1089241559753393 | 8.233503140233994 | 8.4022311729465553 | 8.6002467465515231 | 8.7140748995415223 | 8.8279079629785908 | 8.9488457292780499 | 9.0179684793287258 | 9.0527504514014119
Log Normal y | -1.4961 | -0.98033 | -0.64453 | -0.36979 | -0.1208 | 0.1208 | 0.36979 | 0.64453 | 0.98033 | 1.4961
Chart: Normal
| 2724 | 3324 | 3765 | 4457 | 5433 | 6088 | 6822 | 7699 | 8250 | 8542
Normal y | -1.4961 | -0.98033 | -0.64453 | -0.36979 | -0.1208 | 0.1208 | 0.36979 | 0.64453 | 0.98033 | 1.4961

## Slide 9
LSE of Failures Observed at 393K
9
Chart: Weibull
| 8.0136741428326843 | 8.1961611392829017 | 8.5083542427490322 | 8.5971128145921103 | 8.7966414589409148 | 8.8832242302789943 | 9.0290582747568902 | 9.113388845899733 | 9.2637863476818083 | 9.3370611247553388
y | -2.6638 | -1.7233 | -1.202 | -0.82167 | -0.5086 | -0.23037 | 0.032925 | 0.29903 | 0.59398 | 0.99269
Chart: Exponential
| 3022 | 3627 | 4956 | 5416 | 6612 | 7210 | 8342 | 9076 | 10549 | 11351
y | 0.06968 | 0.17848 | 0.30059 | 0.4397 | 0.60134 | 0.79424 | 1.0335 | 1.3486 | 1.8112 | 2.6985
Chart: Log Normal
| 8.0136741428326843 | 8.1961611392829017 | 8.5083542427490322 | 8.5971128145921103 | 8.7966414589409148 | 8.8832242302789943 | 9.0290582747568902 | 9.113388845899733 | 9.2637863476818083 | 9.3370611247553388
y | -1.4961 | -0.98033 | -0.64453 | -0.36979 | -0.1208 | 0.1208 | 0.36979 | 0.64453 | 0.98033 | 1.4961
Chart: Normal
| 3022 | 3627 | 4956 | 5416 | 6612 | 7210 | 8342 | 9076 | 10549 | 11351
y | -1.4961 | -0.98033 | -0.64453 | -0.36979 | -0.1208 | 0.1208 | 0.36979 | 0.64453 | 0.98033 | 1.4961

## Slide 10
LSE of Failures Observed at 363K
It can be observed from the above figures that the coefficient of correlation is higher and closest to 1 for Weibull distribution
10
Chart: Weibull
| 8.6247912020142561 | 8.8710842639783536 | 9.0449939193881903 | 9.2023082002789192 | 9.3094614628439896 | 9.430037992886092 | 9.5355349686877346 | 9.6369797153157535 | 9.7083846613774405 | 9.7904868134488847
Weibull y | -2.6638 | -1.7233 | -1.202 | -0.82167 | -0.5086 | -0.23037 | 0.032925 | 0.29903 | 0.59398 | 0.99269
Chart: Exponential
| 5568 | 7123 | 8476 | 9920 | 11042 | 12457 | 13843 | 15321 | 16455 | 17863
Exponential y | 0.06968 | 0.17848 | 0.30059 | 0.4397 | 0.60134 | 0.79424 | 1.0335 | 1.3486 | 1.8112 | 2.6985
Chart: Log Normal
| 8.6247912020142561 | 8.8710842639783536 | 9.0449939193881903 | 9.2023082002789192 | 9.3094614628439896 | 9.430037992886092 | 9.5355349686877346 | 9.6369797153157535 | 9.7083846613774405 | 9.7904868134488847
Log Normal y | -1.4961 | -0.98033 | -0.64453 | -0.36979 | -0.1208 | 0.1208 | 0.36979 | 0.64453 | 0.98033 | 1.4961
Chart: Normal
| 5568 | 7123 | 8476 | 9920 | 11042 | 12457 | 13843 | 15321 | 16455 | 17863
Normal y | -1.4961 | -0.98033 | -0.64453 | -0.36979 | -0.1208 | 0.1208 | 0.36979 | 0.64453 | 0.98033 | 1.4961

## Slide 11
Weibull Distribution Parameters for Failures at different Temperatures
Shape and Scale Parameter for Test Temperatures
Temperature (in K) | Shape Parameter | Scale Parameter (in cycles)
403 | 2.734 | 6456.61379
393 | 2.499 | 7967.11698
363 | 2.917 | 13289.6164
11

## Slide 12
Failure CDF Plot vs TTF( hrs ) at different Test
Temperatures
Reliability Plot vs TTF( hrs ) at different Test Temperatures
12

## Slide 13
Determination of Acceleration Factor Graphically.
Averaging of Shape Parameter.
(average) = (403K + 393K + 363K)/3 = 2.717
Revised Scale Parameter is calculated using
Maximum Likelihood Equation
The MTTF values are calculated
using formula
13

## Slide 14
Revised Parameter Values for Test Temperatures
Temperature (in K) | Shape Parameter | Scale Parameter (in hrs) | Mean Time to Failure (in hrs)
403 | 2.717 | 6260.16 | 5568
393 |  | 7817.70 | 6954
363 |  | 12824.19 | 12824
14

## Slide 15
Arhenius Plotting of ln (θ) vs Stress (1/T)
ln(θ) = ln A + B/T
ln A = 2.4286
A = 11.34
B = Ea/R = 2555
Activation Energy =
Ea = 2555 x 8.617 x 10^-5 = 0.22016 eV
15
Chart: ln(θ) vs Stress(1/T)
| 2.4813895781637717E-3 | 2.5445292620865142E-3 | 2.7548209366391185E-3
ln theta | 8.742 | 8.9641 | 9.4591

## Slide 16
Acceleration Factors (AFs)
AFt→u = θ(use)/θ(test)
AF403-298 = /6260 = 1597.44
AF393-298 = /7818 = 1279.09
AF363-298 = /12824 = 779.79
AFs are calculated as below and the normal use life of Relays observed in above three experiments are as below
16

## Slide 17
LSE Fitting of Cumulative Failure data
The cumulative failure data fits Normal Distribution the best

## Slide 18
Inferences
•Overall Failure pattern follows the Normal distribution best
•Arrhenius modelling fits strongly with ln(θ) vs 1/T.
• The mean life of relays as observed from Normal Distribution (of complete failure data) is 8746333 cycles.
18

## Slide 19
Conclusion
•Relay life decreases rapidly with temperature and switching rate
•Estimated mean life under normal use condition is 8746333 cycles
vis-à-vis OEM established life of 10 million cycles
•Failures were dominated by contact wear out
•Relay endurance is strongly influenced by temperature, load and cycle rate
19

## Slide 20
Recommendations
•Matching switching cycle to real‑world conditions
•Improving chamber calibration and uniform airflow
•Usage of wider temperature spacing with larger samples
20

## Slide 21
THANK YOU
21